## Slide 1: DSP-First, 2/e
LECTURE #3
Complex Exponentials
& Complex Numbers

## Slide 2: License Info for SPFirst Slides
This work released under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commerical
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation

## Slide 3: READING ASSIGNMENTS
This Lecture:
  Chapter 2, Sects. 2-3 to 2-5
Appendix A: Complex Numbers
  Appendix B: MATLAB
  Next Lecture: Complex Exponentials

## Slide 4: LECTURE OBJECTIVES
Introduce more tools for manipulating complex numbers
  Conjugate
  Multiplication & Division
  Powers
  N-th Roots of unity

## Slide 5: LECTURE OBJECTIVES
Phasors = Complex Amplitude
  Complex Numbers represent Sinusoids
Next Lecture: Develop the ABSTRACTION:
  Adding Sinusoids = Complex Addition
  PHASOR ADDITION THEOREM

## Slide 6: WHY? What do we gain?
Sinusoids are the basis of DSP,
  but trig identities are very tedious
Abstraction of complex numbers
  Represent cosine functions
  Can replace most trigonometry with algebra
Avoid all Trigonometric manipulations

## Slide 7: COMPLEX NUMBERS
To solve: z2 = -1
  z = j
  Math and Physics use z = i
Complex number: z = x + j y
x
y
z
Cartesian
coordinate
system

## Slide 8: PLOT COMPLEX NUMBERS
Real part:
Imaginary part:

## Slide 9: COMPLEX ADDITION = VECTOR Addition

## Slide 10: *** POLAR FORM ***
Vector Form
  Length =1
  Angle = q
Common Values
    j has angle of 0.5p
    -1 has angle of p
    - j has angle of 1.5p
    also, angle of -j could be -0.5p = 1.5p -2p
    because the PHASE is AMBIGUOUS

## Slide 11: POLAR <--> RECTANGULAR
Relate (x,y) to (r,q)
Need a notation for POLAR FORM
Most calculators do
Polar-Rectangular

## Slide 12: Euler’s FORMULA
Complex Exponential
  Real part is cosine
  Imaginary part is sine
  Magnitude is one

## Slide 13: Cosine = Real Part
Complex Exponential
  Real part is cosine
  Imaginary part is sine

## Slide 14: Common Values of exp(jq)
Changing the angle

## Slide 15: COMPLEX EXPONENTIAL
Interpret this as a Rotating Vector
  q = wt
  Angle changes vs. time
  ex: w=20p rad/s
  Rotates 0.2p in 0.01 secs

## Slide 16: Cos = REAL PART
So,
Real Part of Euler’s
General Sinusoid

## Slide 17: COMPLEX AMPLITUDE
General Sinusoid
Sinusoid = REAL PART of complex exp: z(t)=(Aejf)ejwt
Complex AMPLITUDE = X, which is a constant

## Slide 18: POP QUIZ: Complex Amp
Find the COMPLEX AMPLITUDE for:
Use EULER’s FORMULA:

## Slide 19: POP QUIZ-2: Complex Amp
Determine the 60-Hz sinusoid whose COMPLEX AMPLITUDE is:
Convert X to POLAR:

## Slide 20: COMPLEX CONJUGATE (z*)
Useful concept: change the sign of all j’s
RECTANGULAR: If z = x + j y, then the complex conjugate is z* = x – j y
POLAR: Magnitude is the same but angle has sign change

## Slide 21: COMPLEX CONJUGATION
Flips vector about the real axis!

## Slide 22: USES OF CONJUGATION
Conjugates useful for many calculations
Real part:
Imaginary part:

## Slide 23: Z DRILL (Complex Arith)

## Slide 24: Inverse Euler Relations
Cosine is real part of exp, sine is imaginary part
Real part:
Imaginary part:

## Slide 25: Mag & Magnitude Squared
Magnitude Squared (polar form):
Magnitude Squared (Cartesian form):
Magnitude of complex exponential is one:

## Slide 26: COMPLEX MULTIPLY = VECTOR ROTATION
Multiplication/division scales and rotates vectors

## Slide 27: POWERS
Raising to a power N rotates vector by Nθ and scales vector length by rN

## Slide 28: MORE POWERS

## Slide 29: ROOTS OF UNITY
We often have to solve zN=1
How many solutions?

## Slide 30: ROOTS OF UNITY for N=6
Solutions to zN=1 are N equally spaced vectors on the unit circle!
What happens if we take the sum of all of them?

## Slide 31: Sum the Roots of Unity
Looks like the answer is zero (for N=6)
Write as geometric sum

## Slide 32: Integrate Complex Exp
Needed later to describe periodic signals in terms of sinusoids (Fourier Series)
    Especially over one period

## Slide 33: BOTTOM LINE
CARTESIAN: Addition/subtraction is most efficient in Cartesian form
POLAR: good for multiplication/division
STEPS:
  Identify arithmetic operation
  Convert to easy form
  Calculate
  Convert back to original form

## Slide 34: Harder N-th Roots
Want to solve zN = c
    where c is a complex number

## Slide 35: Euler’s FORMULA
Complex Exponential
  Real part is cosine
  Imaginary part is sine
  Magnitude is one

## Slide 36: Real & Imaginary Part Plots
PHASE DIFFERENCE = p/2

## Slide 37: COMPLEX EXPONENTIAL
Interpret this as a Rotating Vector
  q = wt
  Angle changes vs. time
  ex: w=20p rad/s
  Rotates 0.2p in 0.01 secs

## Slide 38: Rotating Phasor
See Demo on CD-ROM
Chapter 2

## Slide 39: AVOID Trigonometry
Algebra, even complex, is EASIER !!!
Can you recall cos(q1+q2) ?
Use: real part of ej(q1+q2) = cos(q1+q2)

## Slide 40: MULTIPLICATION
CARTESIAN: use polynomial algebra
POLAR: easier because you can leverage the properties of exponentials
Multiply the magnitudes and add the angles

## Slide 41: DIVISION
CARTESIAN: use complex conjugate to convert to multiplication:
POLAR: simpler to subtract exponents

## Slide 42: Complex Numbers
WHY? need to ADD sinusoids
Use an ABSTRACTION
  Complex Amplitude, X, has mag & phase
  Complex Exponential
  Euler’s Formula