## Slide 1: DSP First, 2/e
LECTURE #1
Sinusoids

## Slide 2: License Info for DSPFirst Slides
This work released under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation

## Slide 3: READING ASSIGNMENTS
This Lecture:
  Chapter 2, Sections 2-1 and 2-2
Chapter 1: Introduction
Appendix B: MATLAB
Review Appendix A on Complex Numbers

## Slide 4: CONVERGING FIELDS
EE
CmpE
Math
Applications
Physics
Computer
Science
BIO

## Slide 5: COURSE OBJECTIVE
Students will be able to:
Understand mathematical descriptions of signal processing algorithms and express those algorithms as computer implementations (MATLAB)
What are your objectives?

## Slide 6: WHY USE DSP ?
Mathematical abstractions lead to generalization and discovery of new processing techniques
Computer implementations are flexible
Applications provide a physical context

## Slide 7: Fourier Everywhere
Telecommunications
Sound & Music
  CDROM, Digital Video
Fourier Optics
X-ray Crystallography
  Protein Structure & DNA
Computerized Tomography
Nuclear Magnetic Resonance: MRI
Radioastronomy
Ref: Prestini, “The Evolution of Applied Harmonic Analysis”

## Slide 8: LECTURE OBJECTIVES
Write general formula for a “sinusoidal” waveform, or signal
From the formula, plot the sinusoid versus time
What’s a signal?
  It’s a function of time, x(t)
  in the mathematical sense

## Slide 9: TUNING FORK EXAMPLE
CD-ROM demo
“A” is at 440 Hertz (Hz)
Waveform is a SINUSOIDAL SIGNAL
Computer plot looks like a sine wave
This should be the mathematical formula:

## Slide 10: TUNING FORK A-440 Waveform
Time (sec)

## Slide 11: SPEECH EXAMPLE
More complicated signal (BAT.WAV)
Waveform x(t) is NOT a Sinusoid
Theory will tell us
  x(t) is approximately a sum of sinusoids
  FOURIER ANALYSIS
    Break x(t) into its sinusoidal components
  Called the FREQUENCY SPECTRUM

## Slide 12: Speech Signal: BAT
Nearly Periodic in Vowel Region
  Period is (Approximately) T = 0.0065 sec

## Slide 13: DIGITIZE the WAVEFORM
x[n] is a SAMPLED SINUSOID
  A list of numbers stored in memory
Sample at 11,025 samples per second
  Called the SAMPLING RATE of the A/D
  Time between samples is
    1/11025 = 90.7 microsec
Output via D/A hardware (at Fsamp)

## Slide 14: STORING DIGITAL SOUND
x[n] is a SAMPLED SINUSOID
  A list of numbers stored in memory
CD rate is 44,100 samples per second
16-bit samples
Stereo uses 2 channels
Number of bytes for 1 minute is
  2 X (16/8) X 60 X 44100 = 10.584 Mbytes

## Slide 15: SINES and COSINES
Always use the COSINE FORM
Sine is a special case:

## Slide 16: SINUSOIDAL SIGNAL
FREQUENCY
  Radians/sec
  Hertz (cycles/sec)
PERIOD (in sec)
AMPLITUDE
  Magnitude
PHASE

## Slide 17: EXAMPLE of SINUSOID
Given the Formula
Make a plot

## Slide 18: PLOT COSINE SIGNAL
Formula defines A, w, and f

## Slide 19: PLOTTING COSINE SIGNAL from the FORMULA
Determine period:
Determine a peak location by solving
Zero crossing is T/4 before or after
Positive & Negative peaks spaced by T/2

## Slide 20: PLOT the SINUSOID
Use T=20/3 and the peak location at t=-4

## Slide 21: TRIG FUNCTIONS
Circular Functions
Common Values
  sin(kp) = 0
  cos(0) = 1
  cos(2kp) = 1 and cos((2k+1) p) = -1
  cos((k+0.5) p) = 0

## Slide 22: Radian
https://en.wikipedia.org/wiki/Radian
https://en.wikipedia.org/wiki/Radian#/media/File:Circle_radians.gif

## Slide 23: Problems:
http://dspfirst.gatech.edu/database/?d=homework&chap=2