## Slide 1: DSP First, 2/e
Lecture 15
DTFT: Discrete-Time Fourier Transform

## Slide 2: License Info for DSPFirst Slides
This work released under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation

## Slide 3: READING ASSIGNMENTS
This Lecture:
  Chapter 7, Section 7-1

## Slide 4: Lecture Objective
Generalize the Frequency Response
Introduce DTFT, discrete-time Fourier transform, for discrete time sequences that may not be finite or periodic
Establish general concept of “frequency domain” representations and spectrum that is a continuous function of (normalized) frequency – not necessarily just a line spectrum

## Slide 5: The Frequency Response
LTI
System

## Slide 6: Discrete-Time Fourier Transform
Definition of the DTFT:
Forward DTFT
Inverse DTFT
Always periodic with a period of 2

## Slide 7: What is a Transform?
Change problem from one domain to another to make it easier
Example: Phasors
  Solve simultaneous sinusoid equations (hard)
  Invert a matrix of phasors (easy)
Has to be invertible
  Transform into new domain
  Return to original domain (inverse must be unique)

## Slide 8: Periodicity of DTFT
For any integer m:
1

## Slide 9: Existence of DTFT
Discrete-time Fourier transform (DTFT) exists – provided that the sequence is absolutely-summable
DTFT applies to discrete time sequences, x[n], regardless of length (if x[n] is absolute summable)

## Slide 10: DTFT of a Single Sample
Unit Impulse function

## Slide 11: Delayed Unit Impulse
Generalizes to the delay property

## Slide 12: DTFT of Right-Sided Exponential

## Slide 13: Plotting: Magnitude and Angle Form

## Slide 14: Magnitude and Angle Plots

## Slide 15: Inverse DTFT ?

## Slide 16: SINC Function:
A “sinc” function or sequence

## Slide 17: SINC Function from the inverse DTFT integral
Given a “sinc” function or sequence
Consider an ideal band-limited signal:
Discrete-time Fourier Transform Pair

## Slide 18: SINC Function – Rectangle DTFT pair

## Slide 19: DTFT of Rectangular Pulse
A “rectangular” sequence of length L
Discrete-time Fourier Transform Pair
Dirichlet Function:

## Slide 20: Summary of DTFT Pairs
Right-sided
Exponential
sinc function
is Bandlimited
Delayed Impulse

## Slide 21: Using the DTFT
The DTFT provides a frequency-domain representation that is invaluable for thinking about signals and solving DSP problems.
To use it effectively you must
  know PAIRS: the Fourier transforms of certain important signals
  know properties and certain key theorems
  be able to combine time-domain and frequency domain methods appropriately

## Slide 22: Summary
Discrete-time Fourier Transform (DTFT)
Inverse Discrete-time Fourier Transform